| Stand | Sturdy metal stand |
| --- | --- |
| Focusing | 2-gear focusing (coarse/fine with 1 μm micrometer scale with top focus stop) or 3-gear focusing (coarse) (focus stop), (medium), fine with 1 and 4 μm micrometer scales, Torque coarse focus, adjustable stage height stop |
| Stage stroke | 25 mm |
| Incident light | Sturdy incident light axis with 4x and 5x reflector turrets – 4x reflector turret for BF/DF/POL/DIC and Fluo – 5x reflector turret for BF/POL/DIC and Fluo – Each equipped with the Color-coded Diaphragm Assistant (CDA) The field and aperture iris diaphragms are centerable. Filter magazine with 4 filters – ø 32 mm The following light sources can be adapted to all incident light axes: – 12 V 100 W Halogen, Hg 50, Hg 100, Xe 75 – (Lamp housing series 106Z / 106 / 107/2) |
| Objective turret/ Objectives | 5x BF/DF M32, 6x BF M25 and 7x BF M25 objective turret – HI PLAN EPI Objectives 5x, 10x, 20x – N PLAN EPI Objectives 2.5x–100x – PLAN Fluotar Objectives 1.25x–100x |
| Accessories | Optional magnification changer (1x, 1.5x, 2x) Fixed ergonomic stage (76 x 50 mm), left and right-hand operation or rotating stage (76 x 50 mm) with wear-resistant ceramic surface belong to the standard product line for industrial tasks with stage brackets and condenser holder. Optional measuring stage with display and USB connection (76 x 40 mm) |
| Transmitted light | 12 V 100 W halogen (lamp housing 107/2) Built-in filter magazine 3-position filter holder, 2 positions with 2 filters –> 32 mm The wide range of condensers rounds out the microscope profile for transmitted light applications. |
| Power supply | Stabilized universal power supply unit, 90–230 V for 12 V 30 W |

Leica徕卡DM2500 M金相显微镜